## Slide 1: Incentive Schemes in Railways
M.N.Reddy
Sr.Lecturer/STC/SC

## Slide 2: PAYMENTS BY RESULTS
Need :
Improve productivity by better utilisation of
    manpower,
    M&P
    and covered area.

## Slide 3: INTRODUCTION
Piece work bonus system was in existence in certain workshops like
  Jamalpur
  Kancharpara and
  Perumbur prior to independence.
However the system adopted was varied from workshops to workshop.

## Slide 4: INTRODUCTION
Railway Board took decision to introduce incentive scheme in 1949
The first and formal scheme was introduced in CLW in Dec’1954
The scheme was successful and further it was extended to ICF in 1960.

## Slide 5: REVIEW
Review of productivity revealed that low standard of efficiency could be improved with this scheme.
Provide better control of activity.
More systematic flow of work.
More effort by individual worker.

## Slide 6: SALIENT FEATURES OF THE SCHEME
The basic wages are guaranteed.
Time is the yard stick for measuring work.
The various operations in the workshops are subjected to time study.
The allowed time is so fixed that the workmen of normal ability may earn 33 1/3% bonus.
The allowed time includes all allowances such as fatigue, general handling, gauging and productivity bonus allowance.

## Slide 7: SALIENT FEATURES
Based on the concept that an average worker while working under non-incentive conditions is assumed to be working at a rating of 60 units.
The same worker under incentive conditions would be working at 80 rating.
It means that the average worker would finish the work in ¾ of the allowed time.
Calculation is done on monthly basis, and the gain or loss cannot be carried out to the next month.
The ceiling limit is fixed at 50% of the time taken.

## Slide 8: TYPE OF WORKERS
The Incentive workers are classified as
    Direct workers
    Essential Indirect workers.
    Indirect workers.

## Slide 9
DW: Engaged in work which can be assessed through time studies.
EIW’ S: Those who contribute to the continuity of the work. Whose work cannot be assessed through time studies.
IWS: Who are provided for cleaning etc. do not contribute directly or indirectly.

## Slide 10: TIMING OF OPERATION
- The only check on the efficiency of the Labour is the systematic comparison of time taken with actual time.

## Slide 11: TIME STUDY
Fixation of time standards for each operation.
It is a technique for determining accurately as possible from a limited number of observations.

## Slide 12: RATING
Rating is the assessment of the skill and effort involved in each element.
Different operative workers performing the same job are studied and the results checked by superior rate fixers.

## Slide 13: NORMALISING
On completion of time study the actual times of all the elements in the work cycle should be converted to time @ 80 rating.
Normalized time = Actual time x observed rating
80 i.e.Incentive rating

## Slide 14: Examples of Normalizing
Slow worker: Actual time = 60 minutes
Observed rating = 60
Normalized time = Actual time x observed rating
80 i.e. Incentive rating
= (60 X 60) / 80 = 45 minutes
Fast worker: Actual time = 36 min, Obs rating = 100
Normalized time = (36 X 100) / 80 = 45 minutes

## Slide 15: ALLOWANCES
General handling and contingencies – 12 1/2 %
Gauging on Machining – 5%
Fatigue – 12 ½ to 25%
Production bonus – 33 1/3 %

## Slide 16: CALCULATION OF ALLOWED TIME
Let Normalized time = 1 Hour
Add allowances as under
a) Fatigue 12.5% = 1x0.125 = 0.125
= 1+0.125 = 1.125
b) Contingency 10%=1.125x10 = 0.1125 Hrs
100
= 1.125+0.1125= 1.2375 Hrs
c) Bonus 33 1/3 % = 1.2375x100 = 1.645875 Hrs
3x100
d) Gauging 5% = 5x1.6459= 0.083=1.646+0.083=1.728 (1.65)
100

## Slide 17: Calculation of Incentive
Allowed time will be fixed for each activity as explained earlier.
Incentive earned = Allowed Time –Time taken
    Time taken
    Allowed time for a turning job = 45 min
    Time taken by a worker = 30 min
    Incentive % = (45-30)/30 = 15/30= 50%

## Slide 18: Calculation of Incentive
    Example in a month one worker has worked for 200 hours and earned allowed time of 280 hours.
Incentive % = Allowed Time –Time taken
    Time taken
    = (280-200)/200= 40%
    Money value of incentive = 80X hourly rate
    = 80X Rs.110
    = Rs.8800/-

## Slide 19: SYNTHETIC TIMES
Synthetic times are time standards built up from element times previously obtained from direct time studies.
Time studies are taken to arrive @ synthetic data such as:
      Loading and unloading values.
      Setting up values
      Changing tool values.
      Preparational value.

## Slide 20: EXTRA TIME
Extra time over the allowed time can be allowed due to
Excess machining work required on castings, forgings, bars.
Hard material
Defects in the machine for which worker is not responsible.
Change in batch quantity against a work order.

## Slide 21: JOB CARDS
Job / Squad cards are the basic documents on the basis of which incentive is calculated.
Job/Squad cards should be punched on/ off with aid of time recording clocks.
From the time of punching, the job cards should remain in the custody of time booth clerk.
All completed Job/squad cards should be sent to incentive bonus section with in 48 hours.

## Slide 22: MATERIAL SCRAP
Normally bonus is payable on quantities of work which confirm to specifications.
If inspector certifies, rejections are owing to material scrap, the reject of outturn will also be taken into account upto the % of work done on rejects.

## Slide 23: IDLE TIME DEDUCTION FROM SUPERVISORS
Shop JE’s are responsible for
      Lack of work
      Lack of tools

## Slide 24: IDLE TIME DEDUCTION FROM SUPERVISORS
Idle time of DW’s | Percentage debited
2 – 10% | 10%
5% - 15% | 20%
>15% | No Bonus

## Slide 25: IDLE TIME BOOKING
Idle time can be booked on accounting the following reasons.
    No Power
    Machine Repair
    Lack of Material
    Lack of tools
    Waiting for work
    Crane repair
    Misc

## Slide 26: Group Incentive Scheme
The new scheme namely Group Incentive Scheme has been introduced in Tirupati, Rayanapadu Workshops of this railway during the year 2000.
In this scheme main group is formed from main production shop of the plant. A standard production unit (SPU) will be defined for each incentive production group.
Support shops incentive group formed from various shops in the plant which directly support the activities of shops included under incentive production groups.

## Slide 27: Group Incentive Scheme
The output performance from shops included under support shops can not be quantified in measurable terms.
Support departments incentive group formed from different departments under plant management who directly but essentially support the production activities in the shops.
The output performance can not be quantified in physical units.

## Slide 28: Salient Features of the Group Incentive Scheme
Management approved annual production plan for each incentive production group is defined before each financial year.
For each despatchable product from the group the applicable SPU of product is defined by the IED.
The manpower strength including LR of 12.5% for each production group is required to achieve annual production plan.
Idle hours may be counted only when the power failure at a stretch for a period of 60 minutes.

## Slide 29: Salient Features of the Group Incentive Scheme
This scheme also does not permit plus cards on any account.
Group attendance factor affects the group incentive.
Excessive detention to the coaches in the plant, affect the incentive.
Defects reported by the customer depots will affect the group incentive.
While deciding the outage 70% weightage is given to the individual shop and 30% weightage is given to overall outage.

## Slide 30: Salient Features of the Group Incentive Scheme
Rework reduce the group incentive.
Minimum bonus earning should be 20%.
Maximum ceiling on bonus earning is 50%.

## Slide 31: CLW Vs GIS
The CLW Pattern | Group Incentive Scheme
Introduced in CLW 1958 further extended to ICF and other workshops. | Introduced in Wheel and Axle Plant, Tirupati Workshop, Rayanapadu Workshop and Mancheshwar Workshops .

## Slide 32
CLW | GIS
It is individual based incentive scheme. | It is group based incentive scheme.
Minimum bonus earning is at 33 1/3 %. | Minimum bonus earning at 20%.
Maximum permissible bonus limit 50%. | Maximum permissible bonus limit 50%
Idle time can be booked on account of lack of tools, machine breakdown, non availability of raw materials. | Idle time can be booked only on account of power failure that too for more than one hour.

## Slide 33
CLW | GIS
Once the outturn is dispatched from the shop there is no provision for deduction of incentive for the bad workmanship. | Quality linkage factors are taken into consideration and they effect the outturn.
Group attendance will not affect the incentive of individual. | Group attendance will affect the individual incentive.
Individual shop outturn is taken for bonus calculation. | 70% of individual shop and 30% of the overall outturn is taken for bonus calculation.

## Slide 34
CLW | GIS
Additional no. of days stay of the coaches will not affect the bonus. | Coaches detained in the shops for more than 60 days effect the bonus.
There are no equalising factor for each type of work. | All types of coaches are converted into standard sleeper coaches.
No. of men work on the production control organisation ranges up to 200. | Only 4 to 5 men are required in the Industrial Engineering department.

## Slide 35: THANK YOU